## Slide 1: Android Studio Programming Training
Nuts and Bolts (Team: 4592)

## Slide 2: Point to Point Control System
The FIRST Tech Challenge use a point-to-point system to control their robots
The Robot Controller acts as the “brains” of the robot and is mounted on the frame of the robot.
The Driver Station lets humans interact with the Robot Controller through a wireless connection.

## Slide 3: REV Robotics Expansion Hub
The Expansion Hub lets the Robot Controller talk to the sensors, motors and servo

## Slide 4: Get your Laptop Ready
Install
Install Android Studio https://developer.android.com/studio/
Install
Install GIT
Install
Install FTC App Master https://github.com/ftctechnh/ftc_app

## Slide 5: Installing Android Studio
https://developer.android.com/studio/index.html

## Slide 6: Download the FTC SDK
You can download this from GitHub
http://bit.ly/KNO3-FTCSDK
Download the repository as a zip
Unzip the file
Extract it where you want to develop
For more advanced users:
Clone the gitrepository
Use the .gitlink in Android Studio at
‘VCS > Checkout from Version Control > Git’ (Not GitHub)
Click ‘Clone’
Continue with this tutorial as normal
When you want to update to the latest SDK, click the VCS down arrow and select Merge

## Slide 7: Import SDK
Open Android Studio
If prompted to import settings, select ‘I do not have a previous...’ and click ‘OK’
If shown the setup wizard, choose a standard setup
If a project is open, click ‘File > Close Project’
Click on ‘Import Project’
Select your extracted SDK folder
Android Studio will attempt to import it
Wait until it finishes everything (Watch the progress bar in the bottom right)
You’ll probably be prompted to install missing platforms. Select ‘Install Missing Platforms’
Same for Build Tools
If you are prompted about Instant Run, select no or don’t remind me again. Instant run won’t play well with the SDK!
Press ‘Alt+1’ to open the Project Pane
Click the arrows next to ‘TeamCode’ then ‘java’ to get to your working package

## Slide 8: What is an Op Mode
You write programs called “op modes” (which stands for “operational modes”) to specify the behavior for their robot. These op modes run on the Robot Controller phone after being selected on the Driver Station phone.
The Robot Controller can execute a selected op mode to perform certain tasks during a matc

## Slide 9: FTC SDK OpMode
The OpMode class is one of your options to extend when creating a program
OpMode requires you to create two methods
  init() runs once, when you press the init button on your driver station
  loop() runs repeatedly (more than once per millisecond, if it can) until the Op Mode is stopped on the driver station
OpMode is generally used for Teleop Programs
You should never do anything that will dramatically slow down execution of these methods

## Slide 10: FTC SDK DcMotor
The DcMotorclass provides a way for you to control your motors
You should define your DcMotor in the class body. This makes it a field
In ‘init()’ or before ‘waitForStart()’, you should initialize it
Basic methods
  ‘setPower(double power)’ Sets the power [-1, 1] to run the motor at
  ‘setDirection(DcMotor.Directiondirection)’ Sets the direction to run the motor. You can use this to reverse the direction for ease of use in your code
  ‘setZeroPowerBehavior(DcMotor.ZeroPowerBehaviorbehavior)’ Tells the motor what to do when it receives no power; coast or brake

## Slide 11: Modes for the Motor
RUN WITHOUT ENCODERS
RUN WITHOUT ENCODER: the setPower method does just that. This is the default mode.
STOP AND RESET EnCODERS
STOP AND RESET ENCODER: this mode resets the motor’s encoder. Follow with an idle() command to allow time for the reset.
RUN TO POSITION
RUN TO POSITION: the setPower method causes the motor to drive to the desired encoder count, which is set with setTargetPosition.
RUN USING
ENCODERS
RUN USING ENCODER: the setPower method causes the motor to turn at a specified percentage of its maximum speed, which is set with setMaxSpeed.

## Slide 12: Distance calculation
Four numbers are needed
  Wheel Circumference – DiameterX PI
  Motor Encoder Counts per rotation - Andymark site
  Gear ratio (Drive motor/ driven motor)
Counts per inch
  Count per rotation / (diameter * pi * gear ratio)
  Scale factor – error correction
    Start with 1
    Test for distance x (20-30 runs)
    Scale Factor = x/average

## Slide 13: FTC SDK Servo
The Servo class provides a way for you to control your servos
You should define your Servo in the class body
In ‘init()’ or before ‘waitForStart()’, you should initialize it
Basic methods
  ‘setPosition(double position)’ Sets the position of the servo, [-1, 1]. The servo will begin moving towards this position. Remember that this value is unitless, and only represents the two edges the servo can be driven to

## Slide 14: FTC SDK OpticalDistanceSensor
The Servo class provides a way for you to read information from Optical Distance Sensors/Light sensors
You should define your OpticalDistanceSensorin the class body
In ‘init()’ or before ‘waitForStart()’, you should initialize it
Basic methods
  ‘getLightDetected()’ returns a double between 0.0 and 1.0 representing the amount of light picked up by the sensor, 0 being no light
  ‘enableLed(booleanenable)’ enable as true to turn on the light, as false to turn it off

## Slide 15: FTC SDK Gamepad
This is actually a field in the OpMode and LinearOpMode classes
Accessed from Op Mode via ‘gamepad1’ or ‘gamepad2’
Values
  Float values
    left_stick_x, left_stick_y, right_stick_x, right_stick_y, left_trigger, right_trigger
  Boolean values
    dpad_up, dpad_down, dpad_left, dpad_right, a, b, x, y, guide, start, back, left_bumper, right_bumper, left_stick_button, right_stick_button

## Slide 16: FTC SDK LinearOpMode
The LinearOpMode class is the other option to extend when creating a program
LinearOpMode requires you to create one method
runOpMode() runs once when init is pressed on the driver station, and allows you to sleep the thread
LinearOpModeis generally used for Autonomous Programs
You should use the ‘waitForStart()’ method after you initialize hardware to wait until the run button is pressed

## Slide 17: OpModes
Regular
Predefined method loop() is called repeatedly
Event Based Programming Model
More difficult for beginners
Linear
Traditional linear sequential execution model
Code is started by the OpMode
Programmer provides the loop in the code
Simpler to use and understand

## Slide 18: FTC SDK @TeleOp/@Autonomous
The @TeleOp/@Autonomous annotation tells the Robot Controller app to register your OpMode as an option
It provides two optional properties, however I highly recommend you give a value to ‘name’.
  ‘name’ –Give your Op Mode a name
  ‘group’ –Optionally, you can sort your Op Modes with group names
@TeleOp(name=“TeleOp4592“, group=“Dev”)
@Autonomous(name=“Auto4592“, group=“Dev”)

## Slide 19: Regular OpModes
Your code will override one or more of the following
  init()
    Called once when you select an OpMode. Used for basic initialization
  init_loop()
    Called every 25 ms after you press the INIT button . Main place for initialization
  start()
    Called when START is pressed. Initialization related more closely to the program
  stop()
    Called when STOP button is pressed
  loop()
    Workhorse for all activity. Is called repeatedly every 25 ms until STOP is pressed

## Slide 20: Program Structure -1
// First we identify the package the OpMode belongs to.
package org.firstinspires.ftc.teamcode;
// Now we import the classes we need from the FTC SDK and the Java SDK.
import com.qualcomm.robotcore.eventloop.opmode.Autonomous;
import com.qualcomm.robotcore.eventloop.opmode.OpMode;
import com.qualcomm.robotcore.util.ElapsedTime;
import java.text.SimpleDateFormat;
import java.util.Date;

## Slide 21: Program Structure -2
// Here we register and extend the base OpMode class to be the new NullOp class.
@Autonomous(name="NullOp")
// @Disabled
public class NullOp extends OpMode
{
private String startDate;
private ElapsedTime runtime = new ElapsedTime();
// Here is the init() method. We don't have anything to do here so we could
// have left it out.
@Override
public void init()
{ }

## Slide 22: Program Structure - 3
// Here we are intializing the variables we are using each time we run the OpMode.
@Override
public void init_loop()
{
startDate = new SimpleDateFormat("yyyy/MM/dd HH:mm:ss").format(new Date());
runtime.reset();
telemetry.addData("Null Op Init Loop", runtime.toString());
}
// Here are the start() and stop() methods. We don't have anything to do at those times so we could have left them out.
@Override
public void start()
{ }
@Override
public void stop()
{ }

## Slide 23: Program Structure - 4
// The loop() method is called over and over until the Stop button is pressed.
// The method displays the elapsed run time on the driver stattion using the
// telemtry field of the base OpMode class.
@Override
public void loop()
{
telemetry.addData("Start", "NullOp started at " + startDate);
telemetry.addData("Status", "running for " + runtime.toString());
}
}

## Slide 24: Methods you will use
Init()
//Load the robot configuration here
DcMotor LeftFront = hardwareMap.dcMotor.get(“Left Front Drive”);
LeftFront – The Variable you will use in the program
Left Front Drive – Name used to identify the motor on the Robot phone

## Slide 25: LinearOpMode
You do not override the usual methods init(), loop() etc.
Everything goes in one method
public class OurProg extends LinearOpMode {
public void runOpMode() {
//do initialization stuff here
waitForStart();
do task A
do task B
do task C
}
}

## Slide 26: Linear OpMode example
public void runOpMode() {
DcMotor motor= hardwareMap.dcMotor.get(‘‘motor’’);
waitForStart();
motor.setPower(1);
sleep(10000);
motor.setPower(0);
}

## Slide 27: Helpful Hints! Reuse Code
Put your hardware in a single class that can be shared with OpModes
public void 4592Robot() {
DcMotor motor;
public Robot(HardwareMap hardwaremap) {
motor = hardwareMap.dcMotor.get(‘‘motor’’);
}
public void setMotorPower(double power) {
motor.setPower(power);
}
public double getMotorPosition() {
return motor.getCurrentPosition();
}
}

## Slide 28: Using the Hardware Class
public void runOpMode() {
Robot robot = new 4592Robot(hardwareMap);
waitForStart();
robot.setMotorPower(1);
while (isOpModeActive() &&
robot.getMotorPosition() < 5000) {
telemetry.addData(‘‘Motor: ‘‘, robot.getMotorPosition());
telemetry.update();
}
robot.setMotorPower(0);
}

## Slide 29: Autonomous Programming – Dead Reckoning
Create a new LinearOpMode, define your hardware, then set it up at the beginning of runOpMode()
  Make sure to include a waitForStart() before the rest of your code
A very easy way to increase the accuracy of your autonomous is to set your motors to run with the built-in speed controlling PID loop.
  ‘motor.setMode(DcMotor.RunMode.RUN_USING_ENCODER);’
  Go ahead and do this to all of your drive motors
Set the power of all motors to 1

## Slide 30: Autonomous - Dead Reckoning
@Autonomous(name=“Dead Reckoning”)
Public class DeadReckoning extends LinearOpMode {
private DcMotor frontLeft;
private DcMotor frontRight;
@Override
public void runOpMode() throws InterruptedException {
frontLeft = hardwareMap.dcMotor.get(“Front Left Motor”);
frontRight = hardwareMap.dcMotor.get(“Front Right Motor”);
frontLeft.setDirection(DcMotorSimple.Direction.REVERSE);
frontLeft.setMode(DcMotorSimple.RunMode.RUN_USING_ENCODER);
frontRight.setMode(DcMotorSimple.RunMode.RUN_USING_ENCODER);
waitforStart();
frontLeft.setPower(1);
frontRight.setPower(1);
Thread.sleep(1000)
frontLeft.setPower(0);
frontRight.setPower(0);
}
}

## Slide 31: Autonomous - Servos
@Autonomous(name=“Servo”)
Public class Servo extends LinearOpMode {
private Servo extender;
@Override
public void runOpMode() throws InterruptedException {
extender = hardwareMap.servo.get(“Extender Servo”);
extender.setPosition(0);
waitforStart();
extender.setPosition(1);
Thread.sleep(1000);
extender.setPosition(0);
Thread.sleep(2000);
}
}

## Slide 32: Reading Sensors
Create a new LinearOpMode, don’t forget waitForStart()
  We will create a 4 motor drive train and a ColorSensor called ‘colorSensor’
Create an if statement with condition ‘colorSensor.red() > colorSensor.blue()’ and in the body set the drive motors to 1
  Create an else statement where you set the drive train motors to -1
Use ‘Thread.sleep(1000);’ to wait for 1 second
Stop all the motors
If the sensor sees more red than blue when start is pressed on the Driver Station, the robot will drive forwards for a second. If it sees blue, it will drive backwards

## Slide 33: Code for color sensing
@Autonomous(name=“ColorSense”)
Public class ColorSense extends LinearOpMode {
private ColorSensor colorSensor;
@Override
public void runOpMode() throws InterruptedException {
colorSensor = hardwareMap.colorSensor.get(“Color Sensor”);
colorSensor.setI2cAdderss(I2cAddress.create8bit(0x6c)
waitforStart();
if (colorSensor.red() > colorSensor.blue()) {
do something;
} else {
do something else
}
}
}

## Slide 34: Forward until Sensor
Drive forwards while sensor sees dark surface, then stop
  Start by setting all of the motors to 1
  Create a while loop with condition ‘lightSensor.getLightDetected() < .4’ and an empty body
  Stop all motors
  Motor.setPower(1);
  While(lightSensor.getLightDetected() < .4) { }
  Motor.setPower(0);

## Slide 35: Forward using Encoders
Start by setting all of the motors to 1
Create two integer variables called ‘target’ and ‘current’
  You don’t need to give current a value yet
  Set target equal to an integer number representing encoder ticks (I’ll use 500
You can use specs from andymark’s website, along with your gear ratios and the circumference of the wheel to predict encoder ticks, however, the best way to do it is usually testing it

## Slide 36
@Autonomous(name=“Forward with Encoder”)
Public class ForwardToEncoder extends LinearOpMode {
private DcMotor frontLeft;
private DcMotor frontRight;
@Override
public void runOpMode() throws InterruptedException {
frontLeft = hardwareMap.dcMotor.get(“Front Left Motor”);
frontRight = hardwareMap.dcMotor.get(“Front Right Motor”);
frontLeft.setDirection(DcMotorSimple.Direction.REVERSE);
frontLeft.setMode(DcMotorSimple.RunMode.RUN_USING_ENCODER);
frontRight.setMode(DcMotorSimple.RunMode.RUN_USING_ENCODER);
waitforStart();
frontLeft.setPower(1);
frontRight.setPower(1);
int target = 500;
int current;
do {
current = (frontLeft.getCurrentPosition() + frontRight.getCurrentPosition())2;
} while(current < target);
frontLeft.setPower(0);
frontRight.setPower(0);
}
}

## Slide 37: Turn to Gyro position
We will use a drive train and an GyroSensorcalled ‘gyroSensor’
Start by setting the left motors to 1 and the right motors to 0
Create a while loop with condition ‘Math.abs(targetAngle-gyroSensor.getHeading()) > 2’ and an empty body
After the while loop, stop the motors
When we subtract the heading from the target, we get our error
We take the absolute value to compare it to a tolerance
When the error is less than ±2, exit the loop and stop the robot

## Slide 38
@Autonomous(name=“Turn to Gyro Postion”)
Public class GyroTurn extends LinearOpMode {
private DcMotor frontLeft;
private DcMotor frontRight;
private GyroSensor gyroSensor;
@Override
public void runOpMode() throws InterruptedException {
frontLeft = hardwareMap.dcMotor.get(“Front Left Motor”);
frontRight = hardwareMap.dcMotor.get(“Front Right Motor”);
frontLeft.setDirection(DcMotorSimple.Direction.REVERSE);
frontLeft.setMode(DcMotorSimple.RunMode.RUN_USING_ENCODER);
frontRight.setMode(DcMotorSimple.RunMode.RUN_USING_ENCODER);
gyroSensoe = hardwareMap.gyroSensor.get(“gyro”);
gyroSensor.resetZAxisIntegrator();
waitforStart();
frontLeft.setPower(1);
frontRight.setPower(1);
double targetAngle = 90;
while(Math.abs(targetAngle – gyroSensor.getheading()) > 2) {};
frontLeft.setPower(0);
frontRight.setPower(0);
}
}

## Slide 39: Tank Drive
In loop(), create two double variables, ‘leftSpeed’ and ‘rightSpeed’, setting them equal to ‘gamepad1.left_stick_y’ and ‘gamepad1.right_stick_y’, respectively
Use ‘motor.setPower(leftSpeed)’ to set the power of your drive motors

## Slide 40: Tank Drive
public void loop() {
double leftSpeed = gamepad1.left_stick_y;
double rightSpeed = gamepad1.right_stick_y;
frontLeft.setPower(leftSpeed);
frontRight.setPower(rightSpeed);
}

## Slide 41: Arcade Drive
Create a new OpMode, define your hardware, then set it up in init()
In loop(), create two double variables, ‘speed’ and ‘turn’, setting them equal to ‘gamepad1.right_stick_y’ and ‘gamepad1.right_stick_x’, respectively
Set the left motor’s power to ‘speed + turn’
Set the right motor’s power to ‘speed - turn’

## Slide 42: Arcade Drive Code
@Override
public void loop() {
double speed = gamepad1.right_stick_y;
double turn = gamepad1.right_stick_x;
frontLeft.setPower(speed + turn);
rearLeft.setPower(speed + turn);
frontRight.setPower(speed – turn);
rearRight.setPower(speed – turn);
}

## Slide 43: Car Drive
Create a new OpMode, define your hardware, then set it up in init()
In loop(), create two double variables, ‘speed’ and ‘turn’, setting them equal to ‘gamepad1.right_stick_y’ and ‘gamepad1.right_stick_x’, respectively
Set the left motors’ power to
  ((1 -Math.abs(turn)) * speed +(1 -Math.abs(speed)) * turn +turn + speed) / 2
Set the right motors’ power to
  ((1 -Math.abs(turn)) * speed -(1 -Math.abs(speed)) * turn -turn + speed) / 2

## Slide 44: Car Drive Code
@Override
public void loop() {
double speed = gamepad1.right_trigger – gamepad1.left_trigger;
double turn = gamepad1.left_stick_x;
double leftSpeed = ((1 -Math.abs(turn)) * speed +(1 -Math.abs(speed)) * turn +turn + speed) / 2
double rightSpeed = ((1 -Math.abs(turn)) * speed -(1 -Math.abs(speed)) * turn -turn + speed) / 2
frontLeft.setPower(leftSpeed);
rearLeft.setPower(leftSpeed);
frontRight.setPower(rightSpeed);
rearRight.setPower(rightSpeed);
}

## Slide 45: Move DCMotor / Servo with if/else
if (gamepad2.a) {
DCmotor.setPower(1);
} else {
DCmotor.setPower(0);
}
if (gamepad2.b) {
servo.setPosition(1);
} else {
servo.setPosition(0);
}

## Slide 46: Digital Input Control
if (gamepad2.left_bumper) {
crServo.setPower(1);
} else {
crServo.setPower(0);
}

## Slide 47: Analog input - Joystick Control
Create a double variable called ‘servoPosition’ and set it equal to ‘gamepad2.right_stick_y / 2 + 1’
Here we want to move the servo to a position depending on where the joystick is positioned
The ‘/ 2 + 1’ divides ‘gamepad2.right_stick_y’ by two and adds 1.
Since ‘gamepad2.right_stick_y’ returns a value [-1, 1], we divide our bounds by 2, yielding [-0.5, 0.5], then add 1, [0, 1], resulting in bounds that match the [0, 1] we need to provide setPosition()

## Slide 48: Servo Joystick control
@Override
public void loop() {
double intakeSpeed = gamepad2.right_trigger;
intake.setPower(intakeSpeed);
double crServoPower = gamepad2.left_stick_y;
crServo.setPower(crServoPower);
double servoPosition = gamepad2.right_stick_y /2 + 1;
servoPosition.setPosition(servoPosition);
}